SYSTEM REQUIREMENTS SPECIFICATION (SyRS)
FOR THE
AUTONOMOUS ROVER

Revision: 1.0
Date:	Dec-2015

Prepared by:
Reviewed by:
Approved by:

# 1 Introduction
## 1.1 Purpose
The Rover is being acquired to help ensure emergency response personnel are not sent into an unsafe operating scene.
## 1.2 Document conventions
## 1.3 Intended audience
This System Requirements Specification is intended for the Rover development team to define the functional and performance requirements for the Rover system.
## 1.4 Additional information
## 1.5 Contact information/SyRS team members
## 1.6 References
# 2 System overview
## 2.1 System context
The operating environment of the Autonomous Rover is an indoor operating theater in which the presence of Hazardous Materials is suspected. The operating environment may be under, special circumstances, an outdoor location, with the understanding that the Autonomous Rover is not designed for that type of environment.
## 2.2 System functions
The Rover is required to explore and map an operating theater and return sensor data as required.
## 2.3 User characteristics
2.3.1 Emergency Response Technician
The Hazardous Material Emergency Response Technician, also referred to as the Response Technician, is the sole person allowed and trained to deploy, operate and recover the Autonomous Rover. Depending on the situation, the unit may dispatch one or two Hazmat Emergency Response Technician into a theater of operations.
2.3.2 Maintenance Technician
The Emergency Response unit has one Maintenance Technician on staff that will be qualified to perform any maintenance on the Rover. The maintenance technician is capable of performing basic electronics soldering and assembly. The technician, however, is not qualified to perform high-reliability soldering or "clean room" fabrication/assembly tasks.
# 3 Functional Requirements
The Rover shall support two (2) sensors from the following list:
- IR Sensor;
- explosive gas sensor;
- smoke sensor;
- ammonia sensor;
- IR range finder;
- acoustic (i.e. ultrasound) range finder;
- radioactivity sensor;
- water/liquid sensor;
- light sensor;
- carbon monoxide sensor.
The Rover shall be able to deploy and retract a vertical boom at the end of which a sensor is mounted.
The Rover shall explore a flat room (without holes) autonomously
The Rover shall produce a map of the explored environment
The Rover shall avoid crashing into obstacles
The Rover shall make it possible to download video images collected by a video sensor.
The Rover shall differentiate walls from inclined pathway
The Rover shall avoid falling on its backside
During the mission the Rover should adopt an avoidance and evasion strategy if it encounters a threat or danger.
Once the Rover has completed the mapping and data collection mission, it is to return to the starting point where it was placed at the start of the mission.
It should be possible to abort a mission, at which time the Rover will return to the point where it was placed at the start of the mission.
All collected sensor data and the area map shall be retained during power-down.
It shall be possible to download the map and sensor data from the Rover using a cabled interface.
It shall be possible to download the map and sensor data from the Rover using the Tablet controller.
# 4 Usability Requirements
# 5 Performance Requirements
The Rover electrical power source shall provide an autonomy of at least 10mn
The Rover electrical power source shall provide an autonomy of at least 30mn
# 6 System Interfaces
The only system interfaces for the Rover should be:
- the man-machine interfaces, including:
    + basic controls for manual operations;
    + an Android Tablet controller; or
    + an iPad Tablet controller.
- an optional Alternating Current interface to recharge the Rover power source;
- the Rover controller re-programming/data download interface.
# 7 System Operations
## 7.1 Human system integration requirements
The Rover shall be controllable through an Android application on an Android Tablet.
The Rover shall be controllable through an IoS application on an iPad Tablet.
It should be possible to learn its operation in no more than a one (1) training session.
The Emergency Response Technician should become totally proficient with all operational aspects of the Rover in no more than five (5) training exercices.
A Rover stowed in its utility case shall be transportable by a single person.
## 7.2 Maintainability
It shall be possible for the Emergency Response Technician to replace Rover sensors and the batteries if they are not rechargeable.
## 7.3 Reliability
# 8 System modes and states
# 9 Physical characteristics
## 9.1 Physical requirements
The Rover must be built with the 2 motor Dagu Electronics Rover 5 robot chassis with encoders. (https://www.pololu.com/product/1551)
The Rover must be built with widely available hardware pieces (Arduino, Raspberry Pi)
The Rover must be assembled with limited soldering capabilities
The Rover (excluding the utility case and Tablet controller) shall not cost more than $200USD, including all Phase 1.0 sensors.
## 9.2 Adaptability requirements
# 10 Environmental conditions
The Rover must explore dangerous areas (with many obstacles/holes, etc.)
# 11 System security
# 12 Information management
# 13 Policies and regulations
# 14 System life cycle sustainment
The total price of the Rover, without the sensor payload and sensor mounts, must be less than 200$
# 15 Packaging, handling, shipping and transportation
The Rover must be packageable for flight travel (less than 10Kg including a flight case, handluggage max dimensions)
The Rover shall not weigh more than 10kg, including the transport utility case.
The maximum dimensions of the utility case must be within airline allowed hand luggage.
The utility case shall have sufficient room to carry:
- the Rover;
- a set of batteries to power the Rover plus a spare set;
- the battery charger if required;
- all the sensors; and
- the control Tablet qith its power supply.
# 16 Verification
# 17 Assumptions and dependencies
# 18 Other Requirements
# Appendix A: Terminology/Glossary/Definitions list
# Appendix B: Requirements Traceability Matrix